## Slide 1
Measurement of ionization yields of nuclear recoils in liquid argon using two-phase detector
International Session-Conference of the Section of Nuclear Physics of the Physical Sciences Department of the Russian Academy of Sciences "Physics of fundamental interactions“ dedicated to 50th anniversary of Baksan Neutrino Observatory
June 8, 2017
A. Bondar, A. Buzulutskov, A. Dolgov, E. Grishnyaev, V. Nosov,
V. Oleynikov (speaker), S. Polosatkin, L. Shekhtman, E. Shemyakina, A. Sokolov
Budker Institute of Nuclear Physics (Budker INP), Novosibirsk, Russia
Novosibirsk State University (NSU), Novosibirsk, Russia
Notes: Good morning (arternoon)!
My name is Vladislav Oleynikov.
I am PhD student in Budker Institute of Nuclear Physics.
The theme of my presentation is “Measurement of ionization yields of nuclear recoils in liquid argon using two-phase detector”
0:00 – 0:15

## Slide 2
Outline
Our global objectives and current activity
2. Description of a two-phase Cryogenic Avalanche Detector (CRAD)
3. Our recent results on ionization yields in liquid Ar
4. Future plans
S1/S2 selection technique
Neutron double scattering
5. Summary
Notes: I have divided talk into 5 parts.
First of all I’ll tell you about Our global objectives and current activity.
Then I’ll describe a two-phase Cryogenic Avalanche Detector
In the third part I’ll present our recent results on Ionization yields in LAr.
After this I’ll tell about our Future plans, in particular about S1/S2 selection technique and Neutron double-scattering
And, finally, I’ll give summary of presentation.
0:15 – 1:00

## Slide 3
Our global objective and current activity
Development of liquid Ar detectors of ultimate sensitivity for dark matter search and coherent neutrino-nucleus scattering experiments and their energy calibration.
Our group is currently conducting researches in the following directions, in the frame of Laboratory of Cosmology and Elementary Particles (NSU and BINP) and in the frame of DarkSide experiment:
Measurement of electroluminescence (EL) yields in two-phase Ar using a 9-liter detector.
Problem of Ar doping with Xe and N2.
Measurement of ionization yields of nuclear recoils in liquid Ar using neutron scattering technique.
Development of new readout technique in two-phase Ar detectors using SiPM-matrices.
Notes: Our global objectives are
Development of liquid Ar detectors of ultimate sensitivity for dark matter search and coherent neutrino nucleus scattering experiments and their energy calibration.
Our group is currently conducting researches in the following directions, in the frame of Laboratory of Cosmology and Elementary Particles (located at the NSU and the BINP) and DarkSide experiment.
Measurement of electroluminescence (EL) yields in two-phase Ar using a 9-liter detector.
Problem of Ar doping with Xe and N2.
Measurement of ionization yields of nuclear recoils in liquid Ar using neutron scattering technique.
Development of new readout technique in two-phase Ar detectors using SiPM-matrices.
1:00 – 2:00

## Slide 4
Experimental setup
A vacuum-insulated 9-liter two-phase cryogenic chamber filled with 2.5 liters of liquid Ar
Neutron
generator
Assembly with EL gap and PMT readout
Notes: Our Experimental setup comprises a vacuum-insulated 9 liters two-phase cryogenic chamber filled with 2.5 liters of liquid Ar.
An assembly with EL gap and PMT readout is located inside the cryogenic chamber and a neutron generator is placed under one.
During each cooling procedure Ar was purified from electronegative impurities by Oxisorb filter, providing electron lifetime in the liquid >70 us. (откуда это число?)
2:00 – 3:00

## Slide 5
Cryogenic chamber
Hamamatsu
S13360-6050PE
6x6 mm2
11x11 matrix
Drift region
EL gap
PMT
The cryogenic chamber included a cathode electrode, two field-shaping electrodes, a THGEM0, immersed in liquid Ar layer and a double-THGEM assembly, consisting of a THGEM1 and THGEM2, placed in the gas phase above the liquid.
Notes: The cryogenic chamber included a cathode electrode, two field-shaping electrodes, a THGEM0, immersed in liquid Ar layer
and a double-THGEM assembly, consisting of a THGEM1 and THGEM2, placed in the gas phase above the liquid.
The EL region was formed by the liquid surface and the THGEM1 plate.
There were two ways of optical readout of the EL gap.
Firstly, the gap was viewed by four compact cryogenic PMT, located on the perimeter of the gap.
Secondly, the scintillation in the spectral range other that VUV (NIR, for example) could be recorded using 11 by 11 SiMP matrix.
2:30 – 4:30

## Slide 6
Neutron generator produced in BINP
To produce neutrons, a specially designed neutron generator was used that continuously emitted monoenergetic not collimated neutrons with a kinetic energy of 2.45 MeV obtained in the DD fusion reaction.
The design parameters:
Neutron yield: 105 neutrons/s
Nominal current of ions: 50 uA
Operating voltage: 80 kV
Insulation: SF6, 8 atm
Notes: To produce neutrons a specially designed neutron generator was used that continuously emitted monenergistic not collimated neutrons with a kinetic energy of 2.45 MeV obtained in the DD fusion reaction.
The Design parameters of the neutron generator are:
Neutron yield: 105 neutrons/s (ten to the fifth power)
Rated current of ions: 50 uA (microamps)
Operating voltage: 80 kV (kilovolts)
Insulation: SF6, 8 atm (sulfur hexafluoride at eight atmospheres)
4:30 – 5:30

## Slide 7
Study of proportional EL in two-phase Ar:
EL yields and amplitude spectra
The EL gap yield as a function of the electric field in the gap, measured using PMT or SiPM signals. The amplitude spectrum of the total PMT signal from the EL gap induced by X-ray from a mixture of the Cd and Am radioactive sources.
High EL gap yield of 15 pe/keV (1 pe/e) and good energy resolution of 22% at 60 keV have been reached at an electric field of 7 kV/cm in the EL gap.
Notes: Study of proportional EL in two-phase Ar has been carried out.
The left picture shows the EL gap yield as a function of the electric field in the gap, measured using PMT or SiPM signal.
The right picture shows the amplitude spectrum of the total PMT signal from the EL gap induced by X-ray from a mixture of the Cd and Am radioactive sources.
High EL gap yield: 15 pe/keV (1.4 pe/e) and good energy resolution: 22% at 60 keV have been reached at 7 kV/cm field in the EL gap.
5:30 – 6:30

## Slide 8
The problem of doping Ar with Xe and N2
Photon emission and atomic collision processes in two-phase argon doped with xenon and nitrogen: the most complete compilation over past 50 years (A. Buzulutskov, Eprint 1702.03612).
The problem is currently under study in our group. You can find details in the article.
Notes: Recently, we have presented a comprehensive analysis of photon emission and atomic collision processes in two-phase argon doped with xenon and nitrogen.
The problem is currently under study in our group.
You can find details in the article.
6:30 – 7:30

## Slide 9
Ionization yield
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization.
The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is the ratio of the number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
Recently we have measured ionization yields of nuclear recoils in liquid argon at 80 and 233 keV (EPL, 108 (2014) 12001)
In present work the ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV for several electric fields.
Notes: The experimental setup and its main parameters have been described previously and now we’ll discuss Measurement of the ionization yield.
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization .
The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is ratio of number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
While for liquid Xe there are ample experimental data on such yields, little is known about it in liquid Ar.
Recently we have measured ionization yield of nuclear recoils in liquid argon at 80 and 233 keV (see the picture).
In present work the ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV for several eclectic fields.
7:30 – 10:00

## Slide 10
Measurement of ionization yield: raw signals
The primary ionization charge in liquid Ar was produced by either 60 keV gamma from 241Am or 2.45 MeV neutron from the DD-generator.
A typical oscillogram with a raw signal and an integral spectrum for Am isotope.
The integral spectra for Am, neutron and background runs.
Notes: The primary ionization charge in liquid Ar was produced by either 60 keV gamma from 241Am or 2.45 MeV neutron from DD-generator.
The left picture shows a typical oscillogram with a raw signal and an integral spectrum for Am isotope.
The right picture shows the integral spectra for Am, neutron and background runs.
10:00 – 10:40

## Slide 11
Measurement of ionization yield: experimental and theoretical spectra
To measure the ionization yield we subtracted the background-run contribution from the neutron run. After this we subtracted the gamma-ray contribution, resulting from a radiative capture in surrounding materials. Finally, the pulse integral was normalized to that of 60 keV peak and we found a spectrum end-point in units of ne.
The theoretical spectrum was convolved with an energy resolution function.
The ionization yield was calculated by dividing the end point of experimental spectrum to the theoretical one.
Notes: To measure ionization yield we subtracted the background-run contribution from the neutron run(see the top left picture).
After this we subtracted the gamma-ray contribution, resulted from a radiative capture in surrounding materials (see the bottom left picture).
Finally, the pulse integral was normalized to that of 60 keV peak and we found a spectrum end-point in units of ne (number of electrons escaping recombination with positive ions unit.)
The theoretical spectrum (red curve on the right picture) was convolved with energy resolution function (the result of convolution is black curve).
The Ionization yield was calculated by dividing the end point of experimental spectrum to the theoretical one.
10:40 – 12:10

## Slide 12
Measurement of ionization yield: results
Ionization yield:
5.9 +- 0.8 and 7.4 +- 1 e-/keV at 0.56 and 0.62 kV/cm
A field dependence is well described by Jaffe model (red curve).
A systematic error is dominant and occurs because of using liquid Ar ionization yield of electron recoil for calibration.
Notes: On the graph you can see the ionization yield as a function of electric field for two data sets:
Square for previous data obtained in 2014 and circles for current data.
A field dependence is well described by Jaffe model (red curve ).
A systematic error is dominant and occurs because of using liquid Ar ionization yield of electron recoil for calibration.
12:10 – 13:00

## Slide 13
Towards nuclear recoil selection using S1/S2 signals
Two-phase CRAD
BGO counter
Trigger (BGO counter)
S1
S2
Previously we used spectra subtraction to reject background events, but there is also opportunity to use S2 / S1 as discriminator factor for nuclear and electron recoil.
We irradiated Cryogenic Avalanche Detector by 22Na isotope, which produce two gamma quanta. One of them was detected by BGO counter and produced trigger and another one was detected by CRAD.
Unfortunately, S1 signal is low, so we plan to install additional SiMP matrix on the detector bottom and improve light collection.
Notes: Previously we used spectra subtraction to reject background events, but also there is opportunity to use S2 S1 ratio as discriminator factor for nuclear and electron recoil.
We irradiated Cryogenic Avalanche Detector by sodium 22 isotope, which produce two gamma quanta.
One of them was detected by BGO counter and produced trigger and another one was detected by CRAD.
The right picture shows typical signals from detectors.
Unfortunately, S1 signal is low, so we plan to install additional SiMP matrix on the detector bottom and improve light collection.
13:00 – 14:10

## Slide 14
10cm
n
α
D-D neutron generator
SiPM matrix
n
Cryostat
Neutron double-scattering concept for low-energy calibration in LAr
Having high spatial resolution, of 1 mm, we expect reaching accuracy of about 2o in scattering angle, corresponding to nuclear recoil energy as low as a few keV.
The double-scattering concept has been recently realized in LXe in LUX experiment [arXiv:1608.05381]
Recoil energy dependence as a function of the neutron scattering angle
Notes: When we will reach sufficient light collection, we plan to realize Neutron double-scattering concept.
This concept has been recently realized in LXe in LUX experiment .
The main idea of this experiment was to register scattered neutron again in the TPC.
The left picture shows a scheme of this experiment.
The right picture shows recoil energy dependence as a function of the neutron scattering angle.
Having high spatial resolution in detector, of 1 mm, we expect reaching accuracy of about 2o in scattering angle, corresponding to nuclear recoil energy as low as a few keV
14:10 – 16:00

## Slide 15
Summary
- We have measured the ionization yields of nuclear recoils in liquid Ar using neutron scattering technique, in new ranges of energies and electric fields.
- Neutron double-scattering technique, for low-energy calibration of liquid Ar dark matter detectors, is being developed in our lab.
- We continue to study proportional electroluminescence in two-phase Ar. In particular, we are trying to resolve the problem of doping Ar with Xe and N2 in the two-phase mode.
- These studies are conducted in the frame of R&D program for the DarkSide dark matter search experiment.
Notes: To sum up,
16:00 – 17:00

## Slide 16
Backup slides

## Slide 17
Photon emission and atomic collision processes in two-phase argon doped with xenon and nitrogen
–We present a comprehensive analysis of photon emission and atomic collision processes
in two-phase argon doped with xenon and nitrogen. The dopants are aimed to convert the VUV
emission of pure Ar to the UV emission of the Xe dopant in the liquid phase and to the near
UV emission of the N2 dopant in the gas phase. Such a mixture is relevant to two-phase dark
matter and low energy neutrino detectors, with enhanced photon collection efficiency for primary and secondary scintillation signals.
Based on this analysis, it is shown that Xe dopant may successfully perform its job on VUV-to-UV conversion in the liquid phase even in presence of N2 impurity, if its content does not exceed 50 ppm.

## Slide 18
Novosibirsk group presentation
Novosibirsk group on rare-event instrumentation operates within both Budker Institute of Nuclear Physics (BINP) and Novosibirsk State University (NSU), in the frame of Lab 3 (BINP) and LCEP (Laboratory of Cosmology and Elementary Particles of Physics Department of NSU).
Also, we have recently joined DarkSide20k collaboration.
Group management:
A. Buzulutskov (leader), A. Bondar (deputy director of BINP and dean of Physics Department of NSU), A. Dolgov (head of LCEP).
Group members:
A. Sokolov (senior scientist), L. Shekhtman (leading scientist), V. Nosov (engineer), R. Snopkov (engineer), E. Shemyakina (PHD student), V. Oleinikov (PHD student), A.Chegodaev (technician).
We also collaborate with S. Polosatkin and E. Grishnyaev from Plasma Division (BINP) on DD neutron generator development.
Notes: Novosibirsk group on rare-event instrumentation operates within both Budker Institute of Nuclear Physics (BINP) and Novosibirsk State University (NSU), in the frame of Lab 3 (BINP) and LCEP (Laboratory of Cosmology and Elementary Particles of Physics Department of NSU).
Also, we have recently joined DarkSide20k collaboration

## Slide 19
Towards nuclear recoil selection using S1/S2 signals
Two-phase CRAD
BGO counter
Trigger (BGO counter)
S1
S2
S1 distribution of time delay with respect to the trigger
We irradiated Cryogenic Avalanche Detector by sodium 22 isotope, which produce two gamma quanta.
One of them was detected by BGO counter and produced trigger and another one by CRAD.
On this spectrum we clearly see peak near trigger time, so signals were really from sodium 22 isotope.
Notes: Previously we used spectra subtraction to reject background events.
But also there is opportunity to use S2 S1 ratio as discriminator factor for nuclear and electron recoil.
We irradiated Cryogenic Avalanche Detector by sodium 22 isotope, which produce two gamma quanta.
One of them was detected by BGO counter and produced trigger and another one by CRAD.
The top right picture shows typical signals from detectors.
The bottom right picture shows S1 distribution of time delay with respect to the trigger
On this spectrum we clearly see peak near trigger time, so signals were really from sodium 22 isotope.
Unfortunately, S1 signal is low, so we plan to install additional SiMP matrix on the detector bottom and improve light collection.
13:00 – 14:10

## Slide 20
Optical spectra

## Slide 21
Resolving problem of EL yield is in the progress.
EPL, 94 (2011) 52001
EPL, 112 (2015) 19001
Current result

## Slide 22
Ionization yield
(LXe): 0.7 – 100 keVnr
SCENE experiment (LAr):
17 – 57 keVnr, but in [PE/keVnr]
Notes: The energy calibration of nuclear recoil detectors is of primary importance to rare-event experiments.
Such a calibration, in particular in liquid Ar and Xe detectors media, is usually performed by measuring the ionization yield and scintillation efficiency of nuclear recoil, using neutron elastic scattering on (off ?) nuclei,
which imitating the interaction with dark matter particle or coherently scattered neutrino.
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization [5]. The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is ratio of number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
It depends on deposited energy (E) and on the electric field (epsilon).
While for liquid Xe there are ample experimental data on such yields, little is known about the ionization yield and scintillation efficiency in liquid Ar.
Recently the first results on the ionization yield of nuclear recoils in liquid argon have been presented in the low energy range.
SCENE collaboration presented results from 17 to 57 keV, but in [PE/keVnr], i.e. detector-dependent units.
6.7 keV and from In present work ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV and complements low energy data.

## Slide 23
S1 / S2 separation in LXe
XENON experiment
LUX experiment
Notes: If we use spectrum end point method we can reject background and gamma after radiative capture by spectra subtraction.
In Neutron double-scattering method we should realize another technique.
This technique is based on different ionization density for neutron and gamma, i.e. we will have different S2 S1 ratio.
Top and bottom left images represent logarithmic ratio of S2 and S1 as a function of energy and we can see clear separation between neutron elastic recoil and electron recoil used in XENON experiment
Right picture represent logarithmic ratio of S2 and S1 as a function of S1 used in LUX experiment.

## Slide 24
Chamber 3D - view
Notes: It is 3d model of our installation.
You can see the detector itself on the left picture and detector inside cryogenic chamber on the right picture.
A tube at the bottom of the right image is neutron generator.

## Slide 25
Ionization yield
Our previous results
EPL, 108 (2014) 12001
SCENE experiment
Phys. Rev. Lett., 112
(2014) 171303, 6.7 keVnr
Notes: The experimental setup and its main parameters have been described and now we’ll discuss Measurement of ionization yield.
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization .
The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is ratio of number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
While for liquid Xe there are ample experimental data on such yields, little is known about the ionization yield and scintillation efficiency in liquid Ar.
Recently the first results on the ionization yield of nuclear recoils in liquid argon have been presented in the low energy range: see the top right and the bottom right tables.
Also recently we have measured ionization yield at 80 and 233 keV.
In present work the ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV for several eclectic fields.
7:30 – 10:00

## Slide 26
Ionization yield
Recently we have measured ionization yields of nuclear recoils in liquid argon at 80 and 233 keV (EPL, 108 (2014) 12001)
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization.
The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is ratio of number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
In present work the ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV for several eclectic fields.
Notes: The experimental setup and its main parameters have been described previously and now we’ll discuss Measurement of the ionization yield.
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization .
The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is ratio of number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
While for liquid Xe there are ample experimental data on such yields, little is known about it in liquid Ar.
Recently we have measured ionization yield of nuclear recoils in liquid argon at 80 and 233 keV (see the picture).
In present work the ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV for several eclectic fields.
7:30 – 10:00