## Slide 1
Measurement of ionization yields of nuclear recoils in liquid argon using two-phase detector
Instrumentation for Colliding Beam Physics (INSTR-17)
February – March 2017
A. Bondar, A. Buzulutskov, A. Dolgov, E. Grishnyaev, V. Nosov, V. Oleinikov (speaker), S. Polosatkin , L. Shekhtman, E. Shemyakina, A. Sokolov
Budker Institute of Nuclear Physics (Budker INP), Novosibirsk, Russia
Novosibirsk State University (NSU), Novosibirsk, Russia
Notes: Hello everybody!
My name is Vladislav Oleynikov.
I am PhD student is Budker Institute of Nuclear Physics.
The theme of my presentation is “Measurement of ionization yields of nuclear recoils in liquid argon using two-phase detector”

## Slide 2
Outline
Our group and activity
2. Concept of two-phase Cryogenic Avalanche Detector (CRAD)
3. Recent results obtained using two-phase CRADs:
- Ionization yields in liquid Ar
4. Future plans
Neutron double-scattering
S1 / S2 separation
5. Summary
Notes: I have divided talk into 5 parts.
First of all I’ll tell you about Our group and activity.
Then I’ll describe Concept of two-phase Cryogenic Avalanche Detector (CRAD).
In the third part I’ll present our results about Ionization yields in LAr.
After this I’ll tell about our Future plans.
And, finally, summarize results.

## Slide 3
Novosibirsk group presentation
Novosibirsk group on rare-event instrumentation operates within both Budker Institute of Nuclear Physics (BINP) and Novosibirsk State University (NSU), in the frame of Lab 3 (BINP) and LCEP (Laboratory of Cosmology and Elementary Particles of Physics Department of NSU).
Also, we have recently joined DarkSide20k collaboration.
Group management:
A. Buzulutskov (leader), A. Bondar (deputy director of BINP and dean of Physics Department of NSU), A. Dolgov (head of LCEP).
Group members:
A. Sokolov (senior scientist), L. Shekhtman (leading scientist), V. Nosov (engineer), R. Snopkov (engineer), E. Shemyakina (PHD student), V. Oleinikov (PHD student), A.Chegodaev (technician).
We also collaborate with S. Polosatkin and E. Grishnyaev from Plasma Division (BINP) on DD neutron generator development.
Notes: Novosibirsk group on rare-event instrumentation operates within both Budker Institute of Nuclear Physics (BINP) and Novosibirsk State University (NSU), in the frame of Lab 3 (BINP) and LCEP (Laboratory of Cosmology and Elementary Particles of Physics Department of NSU).
Also, we have recently joined DarkSide20k collaboration

## Slide 4
Our global objective
Development and energy calibration of liquid Ar detectors of ultimate sensitivity for dark matter search and coherent neutrino nucleus scattering experiments.
That means the development of nuclear recoil detectors capable to operate in single-electron and single-photon counting mode and their energy calibration at lower energies.
Notes: Our global objectives are Development and energy calibration of liquid Ar detectors of ultimate sensitivity for dark matter search and coherent neutrino nucleus scattering experiments.
That means the development of nuclear recoil detectors capable to operate in single-electron and single-photon counting mode and their energy calibration at lower energies.

## Slide 5
Ionization yield
Notes: The energy calibration of nuclear recoil detectors is of primary importance to rare-event experiments.
Such a calibration, in particular in liquid Ar and Xe detectors media, is usually performed by measuring the ionization yield and scintillation efficiency of nuclear recoil, using neutron elastic scattering on (off ?) nuclei,
which imitating the interaction with dark matter particle or coherently scattered neutrino.
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization . The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is ratio of number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
It depends on deposited energy (E) and on the electric field (epsilon).
While for liquid Xe there are ample experimental data on such yields, little is known about the ionization yield and scintillation efficiency in liquid Ar.
Recently the first results on the ionization yield of nuclear recoils in liquid argon have been presented in the low energy range: from 17 to 57 keV and point 6.7 keV.
In present work ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV and complements low energy data.

## Slide 6
Experimental setup of two-phase CRAD
Notes: We call our Experimental setup Cryogenic Avalanche Detector or CRAD in short form.
It comprises a vacuum-insulated 9 liters cryogenic chamber filled with 2.5 liters of liquid Ar.
Ar was taken from a bottle with a specified purity of 99.998%
During each cooling procedure Ar was purified from electronegative impurities by Oxisorb filter, providing electron lifetime in the liquid >70 us. (откуда это число?)
The detector was operated in two-phase mode in the equilibrium state, at a saturated vapor pressure of one absolute atmosphere and at temperature of 87.3 Kelvins.
After each cryogenic measurement, the Ar was liquefied from the chamber back to a stainless steel bottle cooled with liquid nitrogen.

## Slide 7
Cryogenic chamber
Notes: The cryogenic chamber included a cathode electrode (made from a THGEM plate), two field-shaping electrodes and a THGEM0, immersed in a 55 mm thick liquid Ar layer.
A 4 mm thick liquid Ar layer above the THGEM) acted as an electron emission region.
A double-THGEM assembly, consisting of a THGEM1 and THGEM2, was placed in the gas phase above the liquid.
The EL region, 18 mm thick, was formed by the liquid surface and the THGEM1 plate.
The voltage applied to the divider varied from 11 to 22 kV, producing an electric drift field in liquid Ar of 0.34 – 0.68 kV / cm, electric emission fields of 2.6 – 5.1 kV / cm and an electric field in the EL gap of 4.0 – 8.0 kV / cm.
There were two ways of optical readout of the EL gap.
Firstly, the gap was viewed by four compact cryogenic PMT, located on the perimeter of the gap.
To prevent discharges and field penetration from the high-voltage region of the EL gap, the PMTs were electrically insulated from the gap a grounded mech and an acrylic protective box of a rectangular shape.
To convert the VUV into the blue light, four wavelength shifter films based on TPB(tetraphenylbutadiene) were deposited on the inner box surface facing the EL gap, in front of each PMT.
Secondly, the scintillation in the spectral range other that VUV (NIR, for example) could be recorded using 11 by 11 SiMP matrix.
To measure ionization yield we have not used double-THGEM multiplier and SiMP matrix.

## Slide 8
Chamber 3D - view
Notes: It is 3d model of our installation.
You can see the detector itself on the left picture and detector inside cryogenic chamber on the right picture.
A tube at the bottom of the right image is neutron generator.

## Slide 9
Neutron generator produced in BINP
The generator includes a high voltage source (Cockcroft-Walton multiplier) and gas-filled neutron-generating tube
Design parameters:
Neutron yield: 105 neutrons/s (DD mode)
Continuous or pulse mode
Rated current of ions: 50 uA
Operating voltage: 80 kV
Insulation: SF6, 8 atm
Notes: To produce neutrons a specially designed neutron generator was used that continuously emitted monenergistic not collimated neutrons with a kinetic energy of 2.45 MeV obtained in the DD fusion reaction.
The generator includes a high voltage source (Cockcroft-Walton multiplier) and gas-filled neutron-generating tube
The Design parameters of neutron generator are:
Neutron yield: 105 neutrons/s (DD mode) (ten to the fifth power)
Continuous or pulse mode
Rated current of ions: 50 uA
Operating voltage: 80 kV
Insulation: SF6, 8 atm (sulfur fluorine four at eight atmospheres)

## Slide 10
PMT1
Measurement of ionization yield: raw signals and a measurement circuit
PMT2
PMT3
PMT4
Amp
CAEN
A1422
Amp
CAEN
N979
∑
CAEN
ADC
LeCroy
PC
Notes: The primary ionization charge in liquid Ar was produced by either 60 keV gamma from Am241 or 2.45 MeV neutron from DD-generator.
On the right top picture a measurement circuit is shown.
On the left picture you can see typical oscillogram with raw signal and integral spectra for neutrons.
On the right bottom picture the integral spectra for gamma, neutrons and background are shown.

## Slide 11
Measurement of ionization yield: experimental and theoretical spectra
Notes: To measure ionization yield one should first determine ne from the spectra.
For this pulse integral should be normalized to that of 60 keV peak and that converted to primary ionization charge.
After subtracting the background-run contribution, the amplitude distribution still contains the gamma-ray background, resulted from radiative capture in surrounding materials.
Gamma rays produced in this reaction have energy above 600 keV, so an energy spectrum due to Compton scattering can be approximated by a linear decreasing function with energy (see top image on the left picture)
On the left picture and bottom image you can see the desired ionization charge spectrum.
The next step is to compare this experimental spectrum to the theoretical one.
The theoretical spectrum was computed using differential cross-section of elastic and inelastic neutron scattering (Black curve on the right picture).
And, finally, this spectrums was convolved with energy resolution function.
Ionization yield was calculated by dividing the end point of experimental spectrum to the theoretical one.

## Slide 12
Measurement of ionization yield: results
Ionization yield:
5.9 +- 0.8 and 7.4 +- 1 e-/keV at 0.56 and 0.62 kV/cm
Field dependence is well described by Jaffe model
Notes: On the graph you can see ionization yield as a function of electric field for two data sets:
Square for previous data obtained in 2014 and circles for current data.
Basically there are two theoretical models that can describe the recombination effect in liquid noble gases: that of Thomas-Imel and that of Jaffe.
Thomas-Imel model predict decreasing function of energy
Red curve is a fit function of Jaffe model.

## Slide 13
Neutron double-scattering concept for energy calibration at low energies: LUX results in LXe
LUX experiment
Notes: The Large Underground Xenon (LUX) experiment is a dual-phase liquid xenon time projection
chamber (TPC) operating at the Sanford Underground Research Facility in Lead, South Dakota.
In the previous year they published results about Low-energy nuclear recoil calibration in LXe.
The main idea of this experiment was to register scattered neutron again in the TPC, called Neutron double-scattering concept.
Using x,y,z reconstructed coordinates for both interaction they found scattering angle theta which is associated with recoil energy according to the following formula.
With this method they measured ionization yield up to 0.7 keV of nuclear recoil.
We want to measure ionization yield in our experiment for LAr using Neutron double-scattering concept too.
But there are some difficulties.

## Slide 14
S1 / S2 separation in LXe
XENON experiment
LUX experiment
Notes: If we use spectrum end point method we can reject background and gamma after radiative capture by spectra subtraction.
In Neutron double-scattering method we should realize another technique.
This technique is based on different ionization density for neutron and gamma, i.e. we will have different S2 S1 ratio.
Top and bottom left images represent logarithmic ratio of S2 and S1 as a function of energy and we can see clear separation between neutron elastic recoil and electron recoil used in XENON experiment
Right picture represent logarithmic ratio of S2 and S1 as a function of S1 used in LUX experiment.

## Slide 15
S1 / S2 separation in LAr
Notes: On the top image you can see time correlation of S1 signal with trigger, produced by double gamma radiation of sodium isotope.
On the bottom image presented S1 S2 correlation.
S1 signal is low because right now we do not have enough acceptance for the S1 signal and separation does not work correctly.
So, we plan to install additional SiMP matrix on the detector bottom and improve light collection.

## Slide 16
Summary
Ionization yields of nuclear recoils in liquid Ar have been measured at higher energies using neutron scattering.

## Slide 17
Backup slides

## Slide 18
Optical spectra

## Slide 19
10cm
n
α
D-D neutron generator
GAPD matrix
n
Cryostat
Neutron double-scattering concept for energy calibration at low energies in LAr
Having high spatial resolution in CRAD, of 1 mm, one can reach accuracy of about 2o in scattering angle, corresponding to nuclear recoil energy as low as a few keV

## Slide 20
Ionization yield
LUX experiment (LXe):
0.7 – 74 keVnr
SCENE experiment (LAr):
17 – 57 keVnr, but in [PE/keVnr]
Notes: The energy calibration of nuclear recoil detectors is of primary importance to rare-event experiments.
Such a calibration, in particular in liquid Ar and Xe detectors media, is usually performed by measuring the ionization yield and scintillation efficiency of nuclear recoil, using neutron elastic scattering on (off ?) nuclei,
which imitating the interaction with dark matter particle or coherently scattered neutrino.
A particle interaction in the liquid phase produces primary scintillation (S1) and ionization [5]. The electrons are drifted away from the interaction site by an electric field and extracted into the gas where they create secondary scintillation (S2).
The ionization yield is ratio of number of electrons escaping recombination with positive ions (ne) and the energy deposited by a nuclear recoil (E).
It depends on deposited energy (E) and on the electric field (epsilon).
While for liquid Xe there are ample experimental data on such yields, little is known about the ionization yield and scintillation efficiency in liquid Ar.
Recently the first results on the ionization yield of nuclear recoils in liquid argon have been presented in the low energy range.
SCENE collaboration presented results from 17 to 57 keV, but in [PE/keVnr], i.e. detector-dependent units.
6.7 keV and from In present work ionization yield of nuclear recoils in liquid Ar has been measured at high energy 233 keV and complements low energy data.